## Slide 1
Joshua Lunn
Speaker
ROBOTICS WITH AI MACHINE VISION
UNITE 2023

## Slide 2
Today's Plan
Introductions
Robotics
Computer Vision
Development Setup
Robot Movement
Make it move
l
What is it? How can we use it?
Arduino IDE setup and code downloaded
How do we control the robot?
We will program the robot to do something
01
02
03
04
05
06

## Slide 3
Joshua Lunn
SW Engineer @ CSLabs
EE Degree from MSU
Founded 2 Startups
Mentor for FTC Robotics Team
AI/ML, Wireless, IoT, Embedded Systems

## Slide 4
Robotics

## Slide 5
Robotics

## Slide 6
Computer Vision
Allows computers to see, observe, and understand.

## Slide 7
Break

## Slide 8
Today's Plan
Introductions
Robotics
Computer Vision
Development Setup
Robot Movement
Make it move
l
What is it? How can we use it?
Arduino IDE setup and code downloaded
How do we control the robot?
We will program the robot to do something
01
02
03
04
05
06

## Slide 9
The Code
HTTPS://BIT.LY/46oE882

## Slide 10
Motors
Rated Voltage
3-6V
Nominal Battery Voltage
3.7V
We have 2 batteries
7.4V

## Slide 11
PWM
analogWrite(pwmAPin, motorSpd);
motorSpd can be 100-255, why not 0 - 255?

## Slide 12
PWM
We have a dead zone from 0 - 100
Rated Voltage of Motor
3-6V
100/255 * 7.4V = 2.9V
Nominal Battery Voltage
3.7V
We have 2 batteries
7.4V

## Slide 13
Tune the robot
Many robots use wheel or motor encoders for determine how far they have traveled
We don't have encoders so the best we can do is tune time and speed to distance

## Slide 14
Break

## Slide 15
Tune the robot
  Measure 3 feet and mark with tape
  Pick a speed between 100-200
  Determine the time (t) needed to make robot stop on the tape
  Tip: Put code in the setup() or add a large delay after the movement so the robot doesn't keep going

## Slide 16
Tune the robot
  Take the time number you came up with and divide by 3, this is your time to go 1 foot
  Now tune for a 90 degree turn
  Can you make the robot make a square and stop?

## Slide 17
josh@thedaringwolf.com
Thank You!